Soil respiration chamber – MZA prototype

I still have to document but this is a fast and ugly overview of the setup

BOM
Electronics:
- MH-Z19 CO2 sensor
- DSB18B20 Temp sensor
- Soil humidity capacitive sensor
- Bluetooth HC-05
- Arduino UNO
- Arduino UNO protoboard
- calibration button
- 4.7k resistance
- LCD 16x2 I2C
Chamber:
- 110mm sanitary pipe

Hardware conections

Component	Pin	Arduino pin
MH-Z19	Gnd	Gnd
MH-Z19	Vcc	5V
MH-Z19	Rx	11
MH-Z19	Tx	10
DSB18B20	Gnd/Black	Gnd
DSB18B20	Vcc/Red	5V
DSB18B20	Signal/Yellow	2 (4.7k resistance)
Humidity sensor	Gnd	Gnd
Humidity sensor	Vcc	3.3V
Humidity sensor	Signal	A0
Bluetooth	Vcc	5V
Bluetooth	Gnd	Gnd
Bluetooth	Tx	0
Bluetooth	Rx	1
LCD I2C	Vcc	5V
LCD I2C	Gnd	Gnd
LCD I2C	SDA
LCD I2C	SCL

Firmware
Libraries:
- new MH-z19 library (can go under 400ppm)
https://github.com/WifWaf/MH-Z19
- Liquid cristal I2C
- dsb18b20
The .ino code is in this folder

Software
We use a python script to read and graph live data coming from serial port.
When the measurement stops the script runs a linear regression of the selected data interval

Pablo Cremades (my electronic local partner also from GOSH) made the script and you can find it here:
https://tecnologias.libres.cc/pablocremades/camara-respiracion-suelo/blob/master/software/GUI/ArduinoPlot.py
If you think we can add some features just drop an issue